## Slide 1: SW Update Over The Air
Ford ECUs Architecture for OTA Solution
On Vehicle Telematics Protocol
OTA Supported Function IDs
  OTA Function ID Flows
  Vector solution for SW Update (FULL Update)

## Slide 2
SYNC4
TCU
ECG
(OVTP Client)
IPC
(OVTP Server)
Ford Cloud
Architecture of OTA (Over-The-Air)
OVTP Over CAN
Wifi
Cellular Network
IPC communicates with ECG via OVTP
Over CAN ONLY regarding OTA

## Slide 3
OVTP (On Vehicle Telematics Protocol) Message
OVTP is a message protocol which is defined by Ford and can be used to communicate between Ford ECU’s applications.
OVTP message
ECG
Client
OTA Manager
IPC
IP: 10.2.0.2
OTA
PARSE
PARSE PUSH
OVTP Payload
OVTP Message
OVTP Header
OVTP Message
Protocol Version
Counter
Crypto type
SSN
Extract by OVTP Layer
OVTP Data which is corresponding to OTA Application

## Slide 4
OVTP on Classical CAN or CAN FD
  Data Link Layer: only 29-bit CAN IDs shall be utilized for OVTP messages on both Classical CAN and CAN FD.

## Slide 5
 | Priority | <Reservaed> | Application | Target (PCM) | Source (TCU)
OVTP Frame | 0b110 | 0b11 | 0b1010 | 0b0000010000 | 0b0010010001
  Binary: 0b110 11 1010 0000010000 0010010001
  Hex: 0x1BA04091
(Tx) 0x1B9180D8 06 41 0F FA 11 D0 29 CC --- Request to Read OTA Data(DID) By Identifier 0xD029
(Rx) 0x1B936060 21 06 00 CC CC CC CC CC --- Pos Resp to Read OTA Data(DID) By Identifier Function 0xD029

## Slide 6
OTA Function Definition
Handle by OVTP Layer
Handle by OTA Application

## Slide 7
OTA Flows

## Slide 8
Vector solution for OTA Stack
Module | Description
CddOvtp | OVTP layer. Session management (open/close/checkstatus) Redirect FIDs/Data to Cddosoh
CddOsoh | OTA Handler OTA FIDs handler Precondition checking for each FID
vSwUpdM | SwUpd Manager Manage SW Update
vMemAccM vMem | Memory Access Manager - Virtual/Physical memory mapping
QSPI | Provide APIs to write to external flash
EcuM
vMemAccM
CanTp
OS
DET
vMem
QSPI Ctrl
vSwUpdM
CddOvtp
CddOsOh
CddOsph
PduR
NvM
DEM
CSM
RTE
Ford App
Get active partition
(image)
Get active partition
(image)
Set active SFMA = addr mode
Set inactive SFMA = OTA mode
PF QSPI Drv
CanIf
Can

## Slide 9
GFX
FBL
IPC Memory Layout (App + GFX)
RH850 D1M1A Internal ROM
00000000
00017FFF
Application
(BSW, Core Apps, HMI control logic)
00022800
003FFFFF
Others
(RAM, KAM, Altia Heap, …)
External ROM (physical address)
Chip A
Chip B
10000000
C0000000
CFBFFFFF
App
CFC00000
CFFDFFFF
Code Flash input
P702_GAS_2.S19
FBL
App
GFX
IPC code
Code Flash
App.hex
App.vbf
gfx.hex
gfx.vbf
Add signature,
Roothash, change to virtual address
Change to address
of external ROM
OTA
EFlashLoad
External Flash
ECG -> IPC
APPL | 0x80020000
GFX | 0x90000000
APPL | 0x1FC00000
GFX | 0x10000000

## Slide 10
VBF Format
VBF Header Type: text |  | header { [description = { "text string row 1" , } ; ] sw_part_number = "XXXXX_XXX_XX"; sw_part_type = EXE; [data_format_identifier = 0x00;] frame_format = CAN_STANDARD; ecu_address = 0x720; [erase = { { 0x10000000, 0x10000000} };] [verification_structure_address = { 0x20000000 };] [sw_signature = { “signature 1”; ] [public_key_hash = “hash”;] file_checksum = checksum; } |  |  |  |  |  | 
Data Type: binary | Data Segment 1 | VBF_Header cont. |  | DS1_StartAddr =(TBD) 0x1000 0000 |  | DS1_Size =(TBD) 0x1000 0000 |  | 
 |  | DS1_Data size=DS1_Size Content: Graphics |  |  |  |  |  | 
 |  |  |  |  |  |  |  | DS1_CS
 | VS subsection | VS_StartAddr =0x803F FE84 | VS_Size =4+40*DS_count |  |  |  |  | 
 |  | VS_Signature size=0x1 00 |  |  |  |  |  | 
 |  |  |  |  | VS_version=0x00 00 | DS_count=0x00 01 | DS1_StartAddr | 
 |  | DS1_Size |  |  |  |  |  | 
 |  | DS1_Hash size=0x20 |  |  |  |  |  | 
 |  |  | VS_CS |  |  |  |  | 
Use to validate SW after OTA finish
Use for Erasing phase (Authorize, Erasing). Note: Virtual Address
Use for prepareActivation (calculate SWASH)
Use for validateLogicalBlock
Data
Signature
RootHash